## Slide 1: Descriptive and inferential statistical methodologies have proven effective in creating a proactive ‘alarm’, accurately identifying Pump Failures with Horse Power (HP) and Pump Efficiency (PE) emerging as key variables of interest with deviations of 15 HP and > 3 % PE being our core signal thresholds.
Note: We’ve included a sample headline for you – you can feel free to use this or modify this as you see fit
Chart: Failure Alarm Chart
Chart: 
| Horse Power | Pump Efficiency | Volumetric Flow Meter 1 | Ambient Temperature | Pump Speed (RPM) | Pump Torque | Volumetric Flow Meter 2
Regression Coefficient | 0.76485 | 0.34237 | 0.050934 | 0.018207 | -0.017867 | -0.018902 | -0.61136

## Slide 2: Descriptive Analysis has enabled us to clearly identify particular signature abnormalities showing clear signature changes in both Rolling Standard Deviation and Rolling Mean Datasets when observed over the respective failure period of interest.
Note: We’ve included a sample headline for you – you can feel free to use this or modify this as you see fit
Chart: Variables Across Time (Rolling Mean)
Chart: Variables Across time (Rolling Standard Dev)

## Slide 3: Further segmentation of the data via binary means (Pump Failure = 0 or 1) illustrated through box and whisker plots show a clear signature difference between that of normal behaviour and that of Failure with Pump Torque, Pump Speed, Pump Efficiency showing the 3 largest variances.
Note: We’ve included a sample headline for you – you can feel free to use this or modify this as you see fit
Raw Data
Rolling Mean Data

## Slide 4: Correlation analyses across datasets yield interesting insights with Ambient Temperature and Pump Torque negatively correlated with Pump Failure in the Rolling Standard Deviation Data, whilst Horse Power and Volumetric Flow Meter show a subsequently strong positive correlation in the Rolling Standard Deviation Dataset.
Chart: PUMP FAILURE CORRELATION COEFFICIENT FOR RAW DATA
| PUMP FAILURE (1 or 0) | Horse Power | Pump Speed (RPM) | Pump Torque | Ambient Temperature | Volumetric Flow Meter 1 | Pump Efficiency | Volumetric Flow Meter 2
PUMP FAILURE (1 or 0) | 1 | 0.42184 | 0.26001 | 0.23318 | 0.20801 | -0.10249 | -0.10268 | -0.11211
Chart: PUMP FAILURE CORRELATION COEFFICIENT FOR ROLLING MEAN DATA
| PUMP FAILURE (1 or 0) | Horse Power | Pump Speed (RPM) | Pump Torque | Ambient Temperature | Volumetric Flow Meter 1 | Pump Efficiency | Volumetric Flow Meter 2
PUMP FAILURE (1 or 0) | 1 | 0.21803 | -0.18417 | -0.21603 | -0.30265 | -0.69244 | -0.69503 | -0.69773
Chart: PUMP FAILURE CORRELATION COEFFICIENT FOR ROLLING STANDAR DEV. DATA
| PUMP FAILURE (1 or 0) | Horse Power | Volumetric Flow Meter 1 | Pump Efficiency | Volumetric Flow Meter 2 | Pump Speed (RPM) | Ambient Temperature | Pump Torque
PUMP FAILURE (1 or 0) | 1 | 0.6901 | 0.64488 | 0.64355 | 0.62592 | 0.62456 | 0.60005 | 0.59726

## Slide 5: Lastly, analysis of the model fit reveals that with a R Squared of .78, a linear model is a good fit for the data with variables Horse Power, Pump Efficiency and Volumetric Flow meter 2 having the largest coefficients, indicative that these variables have the most immediate relationship with respect to Pump Failure behaviour.
Chart: 
| Horse Power | Pump Efficiency | Volumetric Flow Meter 1 | Ambient Temperature | Pump Speed (RPM) | Pump Torque | Volumetric Flow Meter 2
Regression Coefficient | 0.76485 | 0.34237 | 0.050934 | 0.018207 | -0.017867 | -0.018902 | -0.61136